## Slide 1
IT 304 Computer Networks Introduction Week 2-Lecture 2

## Slide 2: Recap: Week 2-Lec 1
Internet
  Big picture View
  Service view
Components of a network
  Edge, access and core
Performance metrics
Cont.. performance metrics
Today’s lecture

## Slide 3: Host: sends packets of data
host sending function:
takes application message
breaks into smaller chunks, known as packets, of length L bits
transmits packet into access network at transmission rate R
  link transmission rate, aka link capacity, aka link bandwidth
R: link transmission rate
host
1
2
two packets,
L bits each
time needed to
transmit L-bit
packet into link
L (bits)
R (bits/sec)
=

## Slide 4: Packet-switching: store-and-forward
takes L/R seconds to transmit (push out) L-bit packet into link at R bps
store and forward: entire packet must arrive at router before it can be transmitted on next link
one-hop numerical example:
L = 7.5 Mbits
R = 1.5 Mbps
one-hop transmission delay = 5 sec
more on delay shortly …
source
R bps
destination
1
2
3
L bits
per packet
R bps
end-end delay = 2L/R (assuming zero propagation delay)

## Slide 5
What are the main components of delay when we use packet switching?
Processing delay
queuing delay
transmission delay
propagation delay

## Slide 6
dtrans: transmission delay: func(L, R)
L: packet length (bits)
R: link bandwidth (bps)
dtrans = L/R
dprop: propagation delay: func(d)
d: length of physical link
s: propagation speed (~2x108 m/sec)
dprop = d/s
Four sources of packet delay
dtrans and dprop
very different
* Check out the online interactive exercises for more examples:
propagation
nodal
processing
queueing
dnodal = dproc + dqueue + dtrans + dprop
A
B
transmission
C
D
Notes: 6

## Slide 7: Four sources of packet delay
dproc: nodal processing
check bit errors
determine output link
typically < msec
dqueue: queueing delay
time waiting at output link for transmission
depends on congestion level of router
propagation
nodal
processing
queueing
dnodal = dproc + dqueue + dtrans + dprop
A
B
transmission

## Slide 8: Queueing delay
R: link bandwidth (bps)
L: packet length (bits)
a: average packet arrival rate
traffic intensity
= La/R
La/R ~ 0: avg. queueing delay small
La/R -> 1: avg. queueing delay large
La/R > 1: more “work” arriving
than can be serviced, average delay infinite!
average queueing delay
La/R ~ 0
La/R -> 1
* Check online interactive animation on queuing and loss

## Slide 9: Delay factor contributions to Total Delay
dprop
  for a link connecting two routers on the same university campus  negligible
  for two routers interconnected by a satellite link(100s km)  100+ milliseconds
dtrans
  > bandwidths (10 Mbps and higher)  negligible [more bits/sec]
  If large Internet packets sent over low-speed dial-up modem links  hundreds of milliseconds .
dproc is often negligible
  Super fast routers

## Slide 10
Propagation delay is defined as the time taken for bits in a packet to go over a transmission link.
A. True
B. False
Propagation delay is a function of
A. Distance
B. Bandwidth
C. Packet size
D. Speed of light in a medium
Tranmission delay is a function of
A. Distance
B. Speed of light in a medium
C. Bandwidth
D. Packet size

## Slide 11
# dtrans | #dprop
# dtrans | #dprop
Total delay =
Total delay =
dEnd-End =N(dproc + dqueue + dtrans + dprop)

## Slide 12: Packet Switching: queueing delay, loss
A
B
C
R = 100 Mb/s
R = 1.5 Mb/s
D
E
queue of packets
waiting for output link
queuing and loss:
if arrival rate (in bits) to link exceeds transmission rate of link for a period of time:
  packets will queue, wait to be transmitted on link
  packets can be dropped (lost) if memory (buffer) fills up

## Slide 13: How do loss and delay occur?
A
B
packets queue in router buffers
packet arrival rate to link (temporarily) exceeds output link capacity
packets queue, wait for turn
packet being transmitted (delay)
packets queueing (delay)
free (available) buffers: arriving packets
dropped (loss) if no free buffers

## Slide 14: Packet loss
queue (aka buffer) preceding link in buffer has finite capacity
packet arriving to full queue dropped (aka lost)
lost packet may be retransmitted by previous node, by source end system, or not at all
A
B
packet being transmitted
packet arriving to
full buffer is lost
buffer
(waiting area)
* Check out the Java applet for an interactive animation on queuing and loss

## Slide 15: Throughput
throughput: rate (bits/time unit) at which bits transferred between sender/receiver
  instantaneous: rate at given point in time
  average: rate over longer period of time
server, with
file of F bits
to send to client
link capacity
Rs bits/sec
link capacity
Rc bits/sec
server sends bits
(fluid) into pipe
pipe that can carry
fluid at rate
Rs bits/sec)
pipe that can carry
fluid at rate
Rc bits/sec)

## Slide 16
If four routers are separated by 10km, but with different capacity optical fibre cables, which delay component will be constant and which one will vary?
A. dprop constant, dtrans varying
B. dprop varying, dtrans varying
C. dprop varying, dtrans constant
D. dprop constant, dtrans constant

## Slide 17: Throughput (more)
Rs < Rc What is average end-end throughput?
Rs bits/sec
Rc bits/sec
Rs > Rc What is average end-end throughput?
link on end-end path that constrains end-end throughput
bottleneck link
Rs bits/sec
Rc bits/sec

## Slide 18: Throughput: Internet scenario
10 connections (fairly) share backbone bottleneck link R bits/sec
Rs
Rs
Rs
Rc
Rc
Rc
R
per-connection end-end throughput: min(Rc,Rs,R/10)
in practice: Rc or Rs is often bottleneck

## Slide 19: “Real” Internet delays and routes
what do “real” Internet delay & loss look like?
traceroute program: provides delay measurement from source to router along end-end Internet path towards destination. For all i:
  sends three packets that will reach router i on path towards destination
  router i will return packets to sender
  sender times interval between transmission and reply.
3 probes
3 probes
3 probes